## Slide 1: Radiation safety and protection

## Slide 2: Sources of radiation exposure
Natural radiation:
Cosmic sources
Terrestrial sources –
              external radiation
              radon
              internal radiation
Man made radiation:
Medical diagnosis and treatment
Consumer and industrial products
Other man made sources

## Slide 3: Cosmic sources
Includes energetic subatomic particles, photons from the sun and supernova & to a lesser extent particles and photons generated by interactions of primary cosmic radiation with atoms and molecules of earths atmosphere
Also includes exposure resulting from airline travel
At sea level, it is about 0.24 mSv/yr
At an elevation of 1600 m, it is 0.50mSv/yr
The global average is 0.4 mSv/yr, about 16% of natural exposure

## Slide 4: Terrestrial sources
It comes from external sources such as soil and from internal sources, including radon and other radionuclides that are inhaled or ingested

## Slide 5: External radiation
From radioactive nuclides in soil, primarily potassium 40 and the radioactive decay products of uranium 238 and thorium 232
Most of the √ radiation comes from top 20 cm of soil
Average exposure rate is about 0.5mSv/yr or approx 20% of average annual background exposure

## Slide 6: Radon
A decay product in the uranium series, is estimated to be responsible for approx 52% of radiation exposure
Radon decays to form solid products that emit  particles
The decay products become attached to dust particles that can be inhaled and deposited on bronchial ept in the respiratory tract

## Slide 7: Other internal radiation
Includes radionuclides taken from external envronment by ingestion
The greatest internal exposure comes from ingestion of uranium and thorium and their decay products
The average exposure is 0.3mSv/yr, about 12% of natural origin exposure

## Slide 8: Dose limits
National Council on Radiation Protection and Measurements (NCRP)
International Commission on Radiological Protection (ICRP)
Dose limits from man made sources for members of the general public, not occupationally exposed is about 10% to that of occupationally exposed individuals
Dentist and their staff are allowed to receive upto 50mSv of whole body radiation exposure/yr

## Slide 9: Patient exposure and dose
Patient dose from dental radiography is usually reported as the amount of radiation received by a target organ
Actual exposure may vary considerably
The most radiosensitive target organs commonly studied include bone marrow, thyroid glands, brain and salivary glands
Mean active bone marrow dose is an important measurement coz bone marrow is the target organ thought responsible for radiation induced leukemia

## Slide 10: Risk estimates
Primary risk from dental radiography is radiation induced cancer
IRCP has developed an estimate that includes probability for induction of both fatal and non fatal cancer and hereditary effects in an exposed population
The degree of risk from exposure to ionizing radiation may be expressed in many ways
It is helpful to compare with equivalent natural exposures
Equivalent natural exposures – the product of effective dose resulting from a specific r/g examination and average daily effective dose delivered by natural sources

## Slide 11: Reducing Dental Exposure
Patient selection criteria
Conducting the examination
  Film and digital imaging
  Intensifying screens and film or digital imaging
  Source to skin distance
  Rectangular collimation
  Filteration
  Leaded aprons and collars
  Film and sensor holders
  Kilovoltage
  Milliampere-seconds
  Film processing
  Interpreting the images
  Protecting personnel
  Quality assurance
  Continuing education

## Slide 12: Reducing dental exposure
3 guiding principles in radiation protection:
Principle of justification – dentist should identify situations where the benefit to the pt from diagnostic exposure exceeds the low risk of harm
Principle of optimization – dentist should use every means to reduce unnecessary exposure to their pt and themselves
Dose limitation – to ensure no individuals are exposed to unacceptably high doses

## Slide 13: Conducting the Examination

## Slide 14: Film and digital imaging
E speed films is almost twice as fasst as speed D and about 50 times as fast as regular dental x ray film
F speed films require about 75% the exposure when compared with E speed film and 40% that of D speed
Digital sensors offer equal or greater dose savings than F speed film and comparable diagnostic utility

## Slide 15: Intensifying screens and film or digital imaging
Compared with older calcium tungstate screens, rare earth screens decrease pt exposure by as much as 55% in panoramic and cephalometric radiography
Dose reduction is not altered by replacing with digital imaging in extraoral r/g

## Slide 16: Source to skin distance
Two standard focal source to skin distance:
20cm (8 inches)
41cm (16 inches)
Results in 32% reduction in exposed tissue volume coz the x ray beam is less divergent
Use of longer source to object distance results in smaller apparent focal spot size thereby increasing resolution

## Slide 17: Rectangular collimation
Federal govt requires that x ray beam be collimated so that the field of radiation at pts skin surface is contained in a circle having a diameter of no more than 7 cm (23/4inches ) when x ray tube is operated above 50 kvp
Amount of radiation scatter generated is proportional to area exposed

## Slide 18: Ways to limit size of x ray beam
Rectangular PID may be attached to tube housing
PID with an exit opening of 3.5x4.4 cm reduces the area of pts skin surface exposed by 60% over that of a round PID (7cm)
A film holding device centres the beam over film or sensor
Film and sensor positioning devices with rectangular collimators may be used with round aiming cyclinders. These holders reduce pt exposure same as compared with rectangular collimators

## Slide 19: Filteration
When x ray beam is filtered with 3mm of aluminium, surface exposure is reduced to about 20% of that with no filteration
Minimum Half-value layer: specific amount of filteration required for dental x ray machines operating at various voltages
1.5mm aluminium total filteration when operating from 50 to 70 kVp
2.5mm aluminium total filteration when operating above 70 kVp

## Slide 20: Leaded aprons and collars
To reduce radiation to gonads and thyroid gland
Thyroid collar is strongly recommended for children and pregnant females as they are especially susceptible to radiation effects

## Slide 21: Film and sensor holders
Holders should be used coz they improve alignment of film or sensor with teeth and x ray machine and reduces unacceptable images
Such devices have an external guide that shows the operator where to align the aiming cylinder

## Slide 22: Kilovoltage
Operating potential of dental x ray machines must range b/w 60-80 kVp
As kVp is lowered, mean energy of beam decreases, resulting in
An image with greater contrast
A beam with many low energy photons
Reduced beam intensity requiring increased exposure time

## Slide 23: Milliampere-seconds
Image density is controlled by quantity of x rays produced. i.e., mA
A r/g of correct density will demonstrate very faint soft tissue outlines
If x ray machine has variable milliampere control, it should be set at highest choice
Coz the film processing conditions are standarized, dentist need to select the proper exposure time

## Slide 24: Film processing
A major cause of unnecessary pt exposure is deliberate overexposure of films compensated by underdevelopment of film
Time-temperature processing, in an adequately equipped and maitained darkroom is best way to ensure optimal film quality
To ensure optimal image quality, dentist should follow films manufacturer recommendations for processing solutions

## Slide 25: Interpreting the images
r/gs are best viewed in semidarkened room with light transmitted through the films
All extraneous lights should be eliminated
Read the r/g with help of magnifying glass
Digital images are best read on a computer screen in a darkened envt

## Slide 26: Protecting personnel
Operator should leave room or be behind barrier or wall during exposure
Walls must be of sufficient density or thickness that the exposure to non occupationally exposed individuals is no greater than 100mGy/wk
Walls constructed of gypsum wallboard are adequate

## Slide 27: Position and distance rule
Operator should stand atleast 6 ft (2mt) from pt, at an angle of 90 to 135 degrees to the central ray of x ray beam
Advantages: inverse square law is applied to reduce exposure to operator
Pts head absorbs most scatter radiation

## Slide 29
Film or sensor holding instruments should be used
Neither operator or pt should hold radiographic tube housing during exposure. Suspension arms should be adequately maintained to prevent housing movement and drift
Personnel-monitoring devices or film badges is preferred

## Slide 30: Quality assurance
Is defined as any planned activity to ensure that a dental office will consistently produce high quality images with minimum exposure to pts and personnel
QA protocols for x ray machine, imaging receptor, film processing, dark room and leaded aprons and thyroid collars should be developed and implemented for each dental health care setting
Reducing unnecessary pt exposure by improper exposure techniques, film processing, and darkroom procedures

## Slide 31: Continuing education
Practitioners should remain informed about safety updates and the availability of new equipment, supplies and techniques that could further improve the diagnostic quality of radiographs and decrease radiation exposure