## Slide 1: Purification of Water
Presenter-
DR.BHAGWAT KENDRE

## Slide 2
CONTENTS
Types
Purification of water on a large scale
Storage
Filtration
Types of filters
1. Biological or slow sand filters
- Elements of a slow sand filter
2. Rapid sand or mechanical filters
- Steps in rapid sand filters
Disinfection
- Action of chlorine
- Principles of chlorination
- Method of chlorination

## Slide 3
Purification of water on a small scale
(1) Household purification of water
Methods
A) Boiling
B) Chemical disinfection
C) Filtration
(2) Disinfection of Wells
Steps in well disinfection
The double pot method
Conclusion
References

## Slide 4
Types
1. Purification of water on a large scale
2. Purification of water on a small scale

## Slide 5
Purification of water on a large scale
Introduction
The purpose of water treatment is to produce water that is safe and wholesome.
The method of treatment depends upon the nature of raw water, and the desired standards of water quality.
For example, ground water (e.g., wells and springs) may need no treatment, other than disinfection.
Surface water (e.g., river water) which tends to be turbid and polluted requires extensive treatment.

## Slide 6
The components of a typical water purification system comprise one or more of the following measures:
I. Storage
II. Filtration
III. Disinfection

## Slide 7
Storage
Storage provides a reserve of water from which further pollution is excluded.
As a result of storage, a very considerable amount of purification takes place.
This is natural purification.

## Slide 8
Physical:
About 90 per cent of the suspended impurities settle down in 24 hours by gravity.
The water becomes clearer.
This allows penetration of light, and reduces the work of the filters.

## Slide 9
(b) Chemical:
The aerobic bacteria oxidize the organic matter present in the water with the aid of dissolved oxygen.
The content of free ammonia is reduced and a rise in nitrates occurs.

## Slide 10
(c) Biological:
The pathogenic organisms gradually die out.
It is found that when river water is stored the total bacterial count drops by as much as 90 per cent in the first 5-7 days.
The optimum period of storage of river water is to be about 10-14 days.
If the water is stored for long periods, there is development of vegetable growths such as algae which impart a bad smell and colour to water.

## Slide 11
(II) FILTRATION
Filtration is the second stage in the purification of water.
It is an important stage because 98-99 per cent of the bacteria are removed by filtration.

## Slide 12
Types of filters
Biological or slow sand filters
Rapid sand or mechanical filters

## Slide 13
SLOW SAND OR BIOLOGICAL FILTERS
Slow sand filters were first used for water treatment in 1804 in Scotland and subsequently in London.
During the 19th century their use spread throughout the world.
Even today, they are generally accepted as the standard method of water purification.

## Slide 14
Elements of a slow sand filter
these consist of:
(1) Supernatant (raw) water
(2) A bed of graded sand
(3) An under-drainage system; and
(4) A system of filter control valves

## Slide 15
Supernatant water
The supernatant water above the sand bed, whose depth varies from 1 to 1.5 metre.
It provides a constant head of water so as to overcome the resistance of the filter bed and thereby promote the downward flow of water through the sand bed.
It provides waiting period of some hours for the raw water to undergo partial purification by sedimentation, oxidation and particle agglomeration.

## Slide 16
(2) Sand bed
The most important part of the filter is the sand bed.
The thickness of the sand bed is about 1 metre.
The sand grains are carefully chosen so that they are rounded and have an "effective diameter" between 0.2 and 0.3 mm.
The sand should be clean and free from clay and organic matter.
The sand bed is supported by a layer of graded gravel 30- 40 cm deep.

## Slide 17
Vital layer
The surface of the sand bed covered with a slimy growth known as vital layer, zoogleal layer or biological layer.
This layer is slimy and gelatinous.
It consists of threadlike algae and numerous forms of life including plankton, diatoms and bacteria.
The formation of vital layer is known as "ripening" of the filter.

## Slide 18
It may take several days for the vital layer to form fully, and when fully formed it extends for 2 to 3 cm into the top portion of the sand bed.
The vital layer is the "heart" of the slow sand filter.
It removes organic matter, holds back bacteria and oxidizes ammoniacal nitrogen into nitrates and helps in bacteria-free water.
Until the vital layer is fully formed, the first few days filtrate is usually run to waste.

## Slide 19
(3) Under -drainage system
At the bottom of the filter bed is the under-drainage system.
It consists of porous or perforated pipes which serve as-
- providing an outlet for filtered water, - supporting the filter medium above.
Once the filter bed has been placed, the under-drainage system cannot be seen.

## Slide 20
Filter box:
The first 3 elements (e.g. supernatant water, sand bed and under-drainage system) are contained in the filter box.
The filter box is an open box.
It usually rectangular in shape, from 2.5 to 4 metres deep.
It is built wholly or partly below ground.
The walls may be made of stone, brick or cement.

## Slide 21
The filter box consists from top to bottom :
Supernatant water …….. 1 to 1.5 metre
Sand bed ……… 1.2 metre
Gravel support …….. 0.30 metre
Filter bottom …….. 0.16 metre

## Slide 22
(4) Filter control
The purpose of these devices is to maintain a constant rate of filtration.
An important component of the regulation system is the "Venturi meter" which measures the bed resistance or "loss of head".
When the resistance builds up, the operator opens the regulating valve so as to maintain a steady rate of filtration.

## Slide 23
Filter cleaning:
Normally the filter may run for weeks or even months without cleaning.
When the bed resistance increases to such an extent that the regulating valve has to be kept fully open, it is time to clean the filter bed.
At this stage, the supernatant water is drained off, and the sand bed is cleaned by "scraping" off the top portion of the sand layer.

## Slide 24
The advantages of a slow sand filter are:
(1) simple to construct and operate
(2) the cost of construction is cheaper than that of rapid sand filters
(3) the physical, chemical and bacteriological quality of filtered water is very high.
(4) When working ideally, slow sand filters have been shown to reduce total bacterial counts by 99.9 to 99.99 per cent and E. coli by 99 to 99.9 per cent.

## Slide 25
RAPID SAND OR MECHANICAL FILTERS
In 1885, the first rapid sand filters were installed in the USA.
Types
Gravity type (e.g. Paterson's filter) and
Pressure type (e.g. Candy’s filter).

## Slide 26
Steps :
Coagulation
Rapid mixing
Flocculation
Sedimentation
Filtration

## Slide 27
(1) Coagulation:
The raw water is first treated with a chemical coagulant such as alum.
The dose of which varies from 5-40 mg or more per litre, depending upon the turbidity and colour, temperature and the pH value of the water.

## Slide 28
(2) Rapid mixing:
The treated water is then subjected violent agitation in a "mixing chamber" for a few minutes.
This allows a quick and thorough dissemination of alum throughout the bulk of the water, which is very necessary.

## Slide 29
(3) Flocculation:
The next phase involves a slow and gentle stirring of the treated water in a "flocculation chamber" for about 30 minutes.
The mechanical type of flocculator is the most widely used.
It consists of a number of paddles which rotate at 2 to 4 rpm.

## Slide 30
(4) Sedimentation:
The coagulated water is led into sedimentation tanks.
It is detained for periods varying from 2-6 hours when the flocculent precipitate together with impurities and bacteria settle down in the tank.
At least 95 per cent of the flocculent precipitate needs to be removed before the water is admitted into the rapid sand filters.
The precipitate or sludge which settles at the bottom is removed from time to time without disturbing the operation of the tank.

## Slide 31
(5) Filtration: The partly clarified water is now subjected to rapid sand filtration.
Filter beds
Each unit of Filter bed has a surface of about 80 to 90 m2.
Sand is the filtering medium.
The “effective size" of the sand particles is between 0.4-0.7 mm.
The depth of the sand bed is usually about 1 metre (2 ½ to 3 Feet).

## Slide 32
Below the sand bed is a layer of graded gravel, 30 to 40 cm. (1-1 ½ feet) deep.
The gravel supports the sand bed and permits the filtered water to move freely towards the under-drains.
The depth of the water on the top of the sand bed is 1.0 to 1 .5 m (5-6 feet).
The under-drains at the bottom of the filter beds collect the filtered water.
The rate of filtration is 5-15 m3/m2/hour.

## Slide 33
Back-washing
Rapid sand filters need frequent washing daily or weekly, depending upon the loss of head.
Washing is accomplished by reversing the flow of water through the sand bed, which is called "back-washing".
Back-washing dislodges the impurities and cleans up the sand bed.
The washing is stopped when clear sand is visible and the wash water is sufficiently clear.
The whole process of washing takes about 15 minutes.
In some rapid sand filters, compressed air is used as part of the back washing processes.

## Slide 34
Advantages
(1) rapid sand filter can deal with raw water directly. No preliminary storage is needed
(2) the filter beds occupy less space
(3) filtration is rapid, 40-50 times that of a slow sand filter
(4) the washing of the filter is easy
(5) there is more flexibility in operation.

## Slide 35
(III) DISINFECTION
CHLORINATION
Chlorination is one of the greatest advances in water purification.
It is supplement, not a substitute to sand filtration.
Chlorine kills pathogenic bacteria, but is has no effect on spores and certain viruses (e.g., polio, viral hepatitis) except in high doses.
Apart from its germicidal effect, chlorine has several important secondary properties in water treatment : it oxidizes iron, manganese and hydrogen sulphide; it destroys some taste and odour-producing constituents; it controls algae and slime organisms; and aids coagulation.

## Slide 36
Action of chlorine:
When chlorine is added to water, there is formation of hydrochloric and hypochlorous acids.
The hydrochloric acid is neutralized by the alkalinity of the water.
The hypochlorous acid ionizes to form hydrogen ions and hypochlorite ions, as follows :-
H2O + Cl2 HCI + HOCI
HOCI H + OCl

## Slide 37
The disinfecting action of chlorine is mainly due to the hypochlorous acid, and to a small extent due to the hypochlorite ions.
The hypochlorous acid is the most effective form of chlorine for water disinfection.
It is more effective (70-80 times) than the hypochlorite ion.
Chlorine acts best as a disinfectant when the pH of water is around 7.

## Slide 38
Principles of chlorination:
Chlorinated water should be clear and free from turbidity.
Chlorine demand of the water should be estimated.
The presence of free residual chlorine for a contact period of at least one hour is essential to kill bacteria and viruses.
The minimum recommended concentration of free chlorine is 0.5 mg/L for one hour.
The sum of the chlorine demand of the specific water plus the free residual chlorine of 0.5 mg/L constitutes the correct dose of chlorine to be applied.

## Slide 39
METHOD OF CHLORINATION
Chlorine is applied either as
(1) chlorine gas
(2) chloramine or
(3) perchloron

## Slide 40
Chlorine gas
It is the first choice, because it is cheap, quick in action, efficient and easy to apply.
chlorine gas is an irritant to the eyes and poisonous.

## Slide 41
Chloramines
Chloramines are loose compounds of chlorine and ammonia.
They have a less tendency to produce chlorinous tastes and give a more persistent type of residual chlorine.
The greatest drawback of chloramines is that they have a slower action than chlorine and therefore they are not being used to any great extent in water treatment.
Perchloron
Perchloron or high test hypochlorite (H.T.H.) is a calcium compound which carries 60-70 per cent of available chlorine.

## Slide 42
SUPERCHLORINATION
Superchlorination followed by dechlorination comprises the addition of large doses of chlorine to the water, and removal of excess of chlorine after disinfection, this method is applicable to heavily polluted waters.

## Slide 43
Orthotolidine (OT) Test
Orthotolidine test enables both free and combined chlorine in water to be determined with speed and accuracy.
The test was developed in 1918.
Ozonation
Ozone is a powerful oxidant and has many uses in water treatment, including oxidation of organic chemicals.
It can be used as a primary disinfectant.

## Slide 44
Membrane processes
It is of most significance in water treatment are reverse osmosis, ultrafiltration, microfiltration and nanofiltration.
These processes have traditionally been applied to the production of water for industrial or pharmaceutical applications, but are now being applied to the treatment of drinking water.

## Slide 45
2. Purification of water on a small scale
(1) Household purification of water
Three methods are generally available for purifying water on an individual or domestic scale.
These methods can be used single or in combination.
A) Boiling
B) Chemical disinfection
C) Filtration

## Slide 46
BOILING
Boiling is a satisfactory method of purifying water for household purposes.
To be effective
water must be brought to a "rolling boil" for 10 to 20 minutes.
It kills all bacteria, spores, cysts and ova and yields sterilized water.
Boiling also removes temporary hardness by driving off carbon dioxide and precipitating the calcium carbonate.
The taste of water is altered, but this is harmless.

## Slide 47
(b) CHEMICAL DISINFECTION
(1) Bleaching powder
(2) Chlorine solution
(3) High test hypochlorite
(4) Chlorine tablets
(5) Iodine
(6) Potassium permanganate

## Slide 48
(1) Bleaching powder:
Bleaching powder or chlorinated lime (CaOCl2) is a white amorphous powder with a pungent smell of chlorine.
When freshly made, it contains about 33 percent of "available chlorine".
It is an unstable compound.
On exposure to air, light and moisture, it rapidly loses its chlorine content.
But when mixed with excess of lime, it retains its strength; this is called "stabilized bleach."
Bleaching powder should be stored in a dark, cool, dry place in a closed container that is resistant to corrosion.

## Slide 49
(2) Chlorine solution:
Chlorine solution may be prepared from bleaching powder.
If 4 kg of bleaching powder with 25 per cent available chlorine is mixed with 20 litres of water, It will give a 5 per cent solution of chlorine.
Ready-made Chlorine solutions in different strengths are also available in the market.
Like bleaching powder, the chlorine solution is subject to losses on exposure to light or on prolonged storage.
The solution should be kept in a dark, cool and dry place in a container.

## Slide 50
(3) High test hypochlorite:
High test hypochlorite (HTH) or perchloron is a calcium compound which contains 60 to 70 per cent available chlorine.
It is more stable than bleaching powder and deteriorates much less on storage.
Solutions prepared from HTH are also used for water disinfection

## Slide 51
(4) Chlorine tablets:
Under various trade names (viz., halazone tablets) are available in the market.
They are quite good for disinfecting small quantities of water, but they are costly.
The National Environmental Engineering Research Institute, Nagpur has formulated a new type of chlorine tablet which is 15 times better than ordinary halogen tablets.
These tablets are manufactured in various strengths and are now available in plenty, in the Indian market at a cheap rate.
A single tablet of 0.5 g is sufficient to disinfect 20 litres of water.

## Slide 52
(5) Iodine:
Iodine may be used for emergency disinfection of water.
Two drops of 2 per cent ethanol solution of iodine will be sufficient for one litre of clear water.
A contact time of 20 to 30 minutes is needed for effective disinfection.
Disadvantages
High costs
The element is physiologically active (thyroid activity)

## Slide 53
(6) Potassium permanganate:
Once widely used it is no longer recommended for water disinfection.
It may kill cholera vibrios, but is of little use against other disease organisms.
Disadvantages
Altering the colour, smell and taste of water

## Slide 54
(c) FILTRATION
Water can be purified on a small scale by filtering through ceramic filters such as Pasteur Chamberland filter, Berkefeld filter and "Katadyn" filter.
The essential part of a filter is the "candle" which is made of porcelain in the Chamberland type.
In the Katadyn filter, the surface of the filter is coated with a silver catalyst so that bacteria coming in contact with the surface are killed by the "oligodynamic" action of the silver ions, which are liberated into the water.
Notes: (c) FILTRATION
Water can be purified on a small scale by filtering through ceramic filters such as Pasteur Chamberland filter, Berkefeld filter and "Katadyn" filter.
The essential part of a filter is the "candle" which is made of porcelain in the Chamberland type.
In the Katadyn filter, the surface of the filter is coated with a silver catalyst so that bacteria coming in contact with the surface are killed by the "oligodynamic" action of the silver ions, which are liberated into the water.

## Slide 55
(d) Ultraviolet Irradiation
It is effective against most microorganisms known to contaminate water supplies like bacteria, yeast, viruses, algae, protozoa etc.
Advantages
The exposure is for short period,
No foreign matter introduced and
No taste and odour produced
Overexposure does not result in any harmful effects.
Disadvantages
No residual effect is available
There is lack of a rapid field test for assessing the treatment efficiency
The apparatus needed is expensive

## Slide 56
(e) Multi-stage reverse osmosis purification of water
It is used to make water both chemically and microbiologically potable by reducing the total dissolved solids, hardness, heavy metals and disease causing bacteria, virus, protozoa and cysts.

## Slide 57
(2) Disinfection of wells
Wells are the main source of water supply in the rural areas.
The need often arises to disinfect them, sometimes on a mass scale, during epidemics of cholera and gastroenteritis.
The most effective and cheapest method of disinfecting wells is by bleaching powder.
Potassium permanganate should not be used, as it is not a satisfactory disinfecting agent.

## Slide 58
STEPS IN WELL DISINFECTION
(1) Find the volume of water in a well
(a) Measure the depth of water column ….. (h) metre
(b) Measure the diameter of well ….. (d) metre
(c) Substitute h and d in:
Volume (litres) = 3.14×d2 ×h ×1000
4
(d) One cubic meter: 1,000 litres of water

## Slide 59
(2) Find the amount of bleaching powder required for disinfection
Estimate the chlorine demand of the well water by "Horrock's Apparatus and calculate the amount of bleaching powder required to disinfect the well.
Roughly, 2.5 grams of good quality bleaching powder would be required to disinfect 1,000 litres of water.

## Slide 60
(3) Dissolve bleaching powder in water
The bleaching powder required for disinfecting the well is placed in a bucket (not more than 100 g in one bucket of water) and made into a thin paste.
More water is added till the bucket is nearly three-fourths full.

## Slide 61
(4) Delivery of chlorine solution into the well
The bucket containing the chlorine solution is lowered some distance below the water surface.
Chlorine solution mixes intimately with the water inside the well.

## Slide 62
(5) Contact period
A contact period of one hour is allowed before the water is drawn for use.
(6) Orthotolidine arsenite test
It is good practice to test for residual chlorine at the end of one hour contact.

## Slide 63
THE DOUBLE POT METHOD
It is an improvement devised by the National Environmental Engineering Research Institute, Nagpur, India.
This method uses two cylindrical pots, one placed inside the other.
The inside height and diameter are 30 cm and 25 cm respectively.
A hole 1 cm in diameter is made in each pot; in the inner pot the hole is in the upper portion, near the rim and in the outer pot it is 4 cm above the bottom.
A mixture of I kg of bleaching powder and 2 kg of coarse sand (approx. 2 mm in diameter) is prepared and slightly moistened with water.
this device works satisfactorily for 2-3 weeks in small household wells containing about 4500 litres of water.

## Slide 64
Conclusion
The provision of merely good water supply does not in itself secure freedom from water borne diseases.
People must recognize safe water as a felt health need and give up their old, unhygienic habits of polluting water supplies.

## Slide 65
References
Park’s Textbook of Preventive and Social Medicine. K. Park, 22nd Edition
Wagner, E.G. and Lanoix, J.N. (1959). Water Supply for Rural Areas and Small Communities, WHO.
Huisman, L. and Wood, W.E. (1974). Slow Sand Filtration, WHO, Geneva.
Cox, C.R. (1964). Operation and Control of Water Treatment Processes, WHO, Geneva.

## Slide 66: THANK YOU